## Slide 1
Storyboard
for Print Policy
1/26/2017
Version 1.0

## Slide 2: Approved Print Policy CR
Printer Requirements
  - Minimum Requirement: Printer MAY ignore the IPP attribute sent from Print Client and use the default value to prioritize Print Policies.
  - If there are one or more conflicts between selected print options contained in "Validate-Job" request and defined print policies, Printer MAY return a "preferred-attributes" collection attribute indicating which substitute values will be used to resolve those conflicts.
Print Client Requirements
  - Print Client SHALL support the IPP operation for "preferred-attributes".
  - If the Print Client receives "preferred-attributes" collection sent from the printer, the Print Client SHALL inform the user which print setting options will be used instead.
  Ex. The dialog box may show a message "The printing will be performed with duplex."

## Slide 3: Limitations
Android Printing Framework
Once user taps Print icon, MPS cannot open a print settings screen when MPS gets a preferred-attributes from printer
IPP
Based on the user authentication, Get-Printer-Attributes does NOT provide any user restricted attributes
preferred-attributes is issued only to Validate-Job request
preferred-attributes is sent by printer when printer finds any conflicts in the user selected settings

## Slide 4: Print Policy Workflow
User
Client
Printer
Input user/pass
Set print options
Tap print icon
Send Validate-Job
Return
preferred-attributes
Show
Notification Dialog
Tap OK/CANCEL
Send Print-Job
Find
a conflicts
OK: Continue to print
CANCEL: Cancel the job

## Slide 5: Print Policy Workflow
Input user/pass
Set print options
Tap print icon
Validate-Job
Conflicts happen in settings
preferred-attributes
two-sided-long-edge
monochrome
OK
- Continue to print
CANCEL
- Cancel the print job

## Slide 6: Notification Dialog
MPS ask user to continue printing even though conflict options are changed by printer
MPS displays a conflict options to user
If user selects OK, MPS will continue to print with Policy settings
If user selects CANCEL, MPS will cancel the print job
Notification Message
Policy Setting List
OK/CANCEL
Button

## Slide 7: Appendix: preferred-attributes
1.3 Constraints and "preferred-attributes"
Printers can impose constraints between Job Creation attributes for practical (e.g., duplexing on transparency media), physical (e.g., label printing from a paper tray), and policy (e.g., no color printing for students) reasons. This specification defines two mechanisms on the Client and Printer that allow a Client to discover what those constraints are prior to creating a print job.
Client constraint resolution uses two new Printer attributes that list the constraints and a list of changes used by the printer for resolving them automatically. These attributes allow the Client user interface to present a simple choice to the user when a selection triggers a constraint: revert to the previous settings or make the following additional changes.
Printer constraint resolution uses the Validate-Document and Validate-Job operations. Clients submit a Validate-Document or Validate-Job request with Template attributes that will be used in the actual document or job creation request. If conflicts are present in the supplied Template attributes, the Printer returns a "preferred-attributes" collection attribute indicating which substitute values will be used to resolve those conflicts.
There is no Validate-Subscription operation because subscriptions always enforce attribute
Quoted from PWG 5100.13-2012 - Printer Working Group